## Slide 1: CS 31007 Autumn 2021 COMPUTER ORGANIZATION AND ARCHITECTURE
Indian Institute of Technology Kharagpur
Computer Science and Engineering
Instructors
Rajat Subhra Chakraborty (RSC)
Bhargab B. Bhattacharya (BBB)
Lecture #16, #17: Computer Arithmetic
07 September 2021
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 2
Computer Arithmetic
?
32
32
32
operation
result
a
b
ALU

## Slide 3: So far covered …
Evolution and history of computer design
Basic components of a computer
Instruction Set Architecture (ISA)
CPU Performance
MIPS Instruction Set, Programming
Acknowledgement: Patterson and Hennessy

## Slide 4: Observed so far …
RISC’s underlying principles lead to efficient hardware design
Simplicity favors regularity
Make the common case fast
Smaller is faster
Good design demands good compromises
Acknowledgement: Patterson and Hennessy

## Slide 5: What is inside?
Processor
Control
Datapath
Memory
for storing
instructions and data
Devices
Input
Output
Monitor
Printer
Keyboard
Mouse
ALU
Notes: 1. The input devices bring the object code and input data from the outside world into the computer.

## Slide 6: Arithmetic for Computers
Operations on integers
  Addition and subtraction
  Multiplication and division
  Dealing with overflow
  Hardware implementation of ALU
Floating-point real numbers
  Representation and operations
  Overflow and underflow
  Hardware implementation of FP-operations
§3.1 Introduction

## Slide 7: What determines the execution time of a machine/assembly-level program P when it is run on a machine M?
P consists of a number of machine-level instructions (IC: instruction count);
Each machine instruction requires several clock cycles to complete (CPI: average number of clock cycles per instruction);
Each clock cycle has certain time period (CCT: clock cycle time)
Thus, CPU-time = IC  CPI  CCT
(CPU Performance Equation)

## Slide 8: Clock Timing
Clock period should be large enough to accommodate delays along critical paths in the circuit (longest ones); but not too large – system slows down unnecessarily
Does it mean that CCT is exclusively determined by the critical delay? Once the hardware is designed, is it fixed for a given technology?
.. Oh no, there is a catch!
You can redesign hardware so that delay becomes smaller: (i) using low-depth logic (increases cost!), or (ii) use retiming, i.e., insert additional state elements (FFs) on long logic paths (increases #clock cycles to perform the same task, thus impacting CPI, though CCT is reduced!)

## Slide 9: Execution Cycle
Instruction
Fetch
Obtain instruction from memory
Instruction
Decode
Determine required actions and instruction size
Operand
Fetch
Locate and obtain operand data from memory/register
Execute
Compute result value or status
Result
Store
Deposit results in register/memory for later use
Next
Instruction
Determine successor instruction
computer arithmetic, ALU design
operand-address computation

## Slide 10: MIPS Example
C code:
f = (g + h) - (i + j);
  f, …, j in $s0, …, $s4
Compiled MIPS code:
add $t0, $s1, $s2 add $t1, $s3, $s4 sub $s0, $t0, $t1
Make common operations faster …
Amdahl
Adders must be very efficient: cost, speed

## Slide 11
2’s Complement Integer Arithmetic: Dilemma of Final Carry and Overflow
0 1 0 0
1 0 1 1
+
(+4)
(-5)
1 1 1 1
(-1)
no final carry;
no overflow;
result correct
(-4)
1 1 0 0
0 1 1 0
+
(+6)
1 0 0 1 0
(+2)
final carry discarded;
result still correct;
no overflow
1 0 0 0
1 0 0 0
+
(-8)
(-8)
1 0 0 0 0
(0)
final carry ;
overflow ;
result invalid
0 1 0 0
0 1 0 0
+
(+4)
(+4)
1 0 0 0
(-8)
no final carry;
overflow ;
result invalid
universe:
4-bit 2’s complement arithmetic
Decimal
0
0000
1
0001
2
0010
3
0011
4
0100
5
0101
6
0110
7
0111
2’s Complement
2’s Complement
1111
1110
1101
Decimal
-1
-2
-3
1100
1011
1010
1001
-4
-5
-6
-7
1000
-8

## Slide 12
Overflow Detection Logic: Hardware Solution
B: bn-1, bn-2, ……, b1, b0
S: sn-1, sn-2, ……, s1, s0
A: an-1, an-2, ……, a1, a0
Overflow = an-1bn-1sn-1 + an-1bn-1 sn-1
+
  overflow  adding two positives yields a negative
  or, adding two negatives gives a positive
sign-bit
In MIPS, on detecting overflow, interrupt (exception) is invoked;
add, addi (overflow considered); addu, addiu (overflow ignored)

## Slide 13
Overflow Detection Logic: Another Solution
Carry into MSB ° Carry out of MSB
  For a N-bit ALU: Overflow = CarryIn[N - 1] XOR CarryOut[N - 1]
A0
B0
1-bit
ALU
Result0
CarryIn0
CarryOut0
A1
B1
1-bit
ALU
Result1
CarryIn1
CarryOut1
A2
B2
1-bit
ALU
Result2
CarryIn2
A3
B3
1-bit
ALU
Result3
CarryIn3
CarryOut3 (final carry)
Overflow
X
Y
X XOR Y
0
0
0
0
1
1
1
0
1
1
1
0
Show that these two solutions are logically equivalent

## Slide 14
Compute: X = A + B – C; A, B, C are +ve integers;
X = (A + B) – C
Or,
X = A + (B – C) ?
Hazards of Finite-Precision Arithmetic
The first choice might cause
overflow – invalid result
The second option is safer
x1 x2
(x1 + x2)/2
Binary search
x1 + (x2 – x1)/2  better write this way: safer!

## Slide 15
Saturating Adders
Saturating arithmetic:
When a result is out of range, provide the most positive or the most negative value that is representable
Required in many DSP applications
Adder
Saturation
logic
Overflow
0
1
Courtesy: Behrooz Parhami, UCSB

## Slide 16: Why Adders?
Addition: a fundamental operation
  Basic block of most arithmetic operations
  Address calculation
Faster and faster
How?
  Architectural-level optimization
  Gate-level optimization
  Speed/area trade-off

## Slide 17: Review: 1-bit adder
One-bit Half Adder:
One-bit Full Adder:
Sum = A  B  Cin
Cout = A.B + B.Cin + A.Cin
FA
A
B
Cin
Cout
Sum
Sum = A  B
Cout = A.B
HA
A
B
Cout
Sum
A B Sum Cout
0 0 0 0
0 1 1 0
1 0 1 0
1 1 0 1
Cin A B Sum Cout
0 0 0 0 0
0 0 1 1 0
0 1 0 1 0
0 1 1 0 1
1 0 0 1 0
1 0 1 0 1
1 1 0 0 1
1 1 1 1 1
Notes: Can we use HA to add two n-bit numbers? No! Carry propagation.

## Slide 18: n-bit Ripple-Carry Adder (RCA)
To add two n-bit numbers
C0
FA
a0
s0
b0
FA
a1
s1
b1
FA
a2
s2
b2
FA
an-1
sn-1
bn-1
Cn
. . .
N-bit RCA delay = n * 
 = (delay of 1-bit FA)
FA
A
B
Cin
Cout
Sum
Critical path in an n-bit ripple-carry adder
 CCT needs to accommodate long delay
Cost = O(n); delay = O(n)
Flat Combinational Logic
Inputs: an-1, an-2, ……, a1, a0 ,bn-1, bn-2, ……, b1, b0
Outputs: sn-1, sn-2, ……, s1, s0, cn
B: bn-1, bn-2, ……, b1, b0
A: an-1, an-2, ……, a1, a0
Notes: What is C0? C_n?
This architecture is called Ripple-carry adder: the simplest!
Carry delay is important

## Slide 19: 4-bit Ripple-Carry Addition: Example
C0
FA
A0
S0
B0
FA
A1
S1
B1
FA
A2
S2
B2
FA
A3
S3
B3
C4
C1
C2
C3
T=1
0
0
1
0
1
0
0
1
0
0
1
0
0
1
1
1
0
0
0
0
0
0
0
0
0
T=0
B=0101
A=0011
S=0000
S=0110
0
0
1
0
0
1
0
1
T=2
S=0100
0
0
0
1
0
1
0
1
T=3
S=0000
1
0
0
1
0
1
0
1
T=4
S=1000
delay = 4 units; also, overflow has occurred
Notes: The time unit is the delay for one full adder to compute its S and Cout signals
What is the meaning of the intermediate (T=1..3) values of S?
How long should the clock period be?
What effect does the carry chain delay have on the clock frequency?

## Slide 20: Subtraction using 2’s complement

## Slide 21: Multi-bit Adder
MSB LSB

## Slide 22: Ripple-Carry Adder
Chain 1-bit adders together
Carry ripples through the entire chain
Disadvantage: slow

## Slide 23
Possible solutions to mitigate
carry-propagation delay
1. Detect the end of carry propagation rather than wait for
the worst-case time
2. Speed-up propagation using techniques such as
  lookahead
  carry-select
  logarithmic adder
3. Limit carry propagation to within a small number of bits
4. Trade-off: speed (or inversely, delay) versus logic cost

## Slide 24: CS 31007 Autumn 2021 COMPUTER ORGANIZATION AND ARCHITECTURE
Indian Institute of Technology Kharagpur
Computer Science and Engineering
Instructors
Rajat Subhra Chakraborty (RSC)
Bhargab B. Bhattacharya (BBB)
Lecture #18: Computer Arithmetic
13 September 2021
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 25
How to speed up computer arithmetic?
Notes: Good Morning!
The title of today’s tComputer alk is “On some Planar Partitioning Problems”.

## Slide 26: Carry-Lookahead Adder
Instead of RCA, use n independent 1-bit FA-modules working in parallel;
no signal propagation through stages; directly generate all
carry-bits from inputs
C0
FA
A0
S0
B0
FA
A1
S1
B1
FA
A2
S2
B2
FA
A3
S3
B3
C4
C1
C2
C3
RCA
C0
FA
A0
S0
B0
FA
A1
S1
B1
FA
A2
S2
B2
FA
A3
S3
B3
C4
C1
C2
C3
CLA
Notes: In the example,
By looking at (A4,B4), we can say for sure that C5=0, no matter what C4 is.
By looking at (A2,B2), we can say for sure that C3=1.
C3, “generated” by (A2,B2) (or by A0,B0 if you wish), “propagated” as far as C4, and then got “killed” by (A4,B4)
The idea is, can we look at A(3..0) and B(3..0) and determine the value of C4 in one shot?

## Slide 27: Carry-Lookahead Adder
Generate all carry bits directly from inputs, instead of rippling through FA-blocks sequentially
Few notation:
  Generate (gi) and propagate (pi) signals for each bit:
    A column will generate a carry out if ai AND bi are both 1.
  gi = ai bi
    A column will propagate a carry in to the carry out if Ai OR Bi is 1.
  pi = ai + bi
    The carry out of a column (Ci) is:
  ci+1 = ai bi + (ai + bi )ci = gi + pi ci

## Slide 28
Carry Lookahead Adder (CLA): Basic Idea
B: bn-1, bn-2, .., bi ,…,b1, b0
S: sn-1, sn-2, ……, s1, s0
A: an-1, an-2, .., ai…, a1, a0
At the ith stage, carry will be generated for propagation to the next stage if and only if
ai = bi = 1; => gi = ai bi ==> carry-generate function
or either ai or bi = 1, and previous carry ci -1 arrives here;
=> pi = ai + bi => carry-propagate function
+
ith-bit
carry-bit ci

## Slide 29: Carry-Lookahead Adder
Generate all carry bits directly from inputs, instead of rippling through FA-blocks sequentially
Few notation:
  Generate (gi) and propagate (pi) signals for each bit:
    A column will generate a carry out if ai AND bi are both 1.
  gi = ai bi
    A column will propagate a carry in to the carry out if Ai OR Bi is 1.
  pi = ai + bi
    The carry out of a column (Ci) is:
  ci+1 = ai bi + (ai + bi )ci = gi + pi ci

## Slide 30: Carry-Lookahead Adder
    The carry out of a column (Ci) is:
  ci+1 = ai bi + (ai + bi )ci = gi + pi ci
We can visualize carry “generate” and “propagate” functions from another perspective:
Ci+1 = a.b + b. cin + a. cin
= a.b + cin. (a+b)
    A column will generate a carry out if ai AND bi are both 1, i,e., gi = ai bi
    A column will propagate a carry if Ai or Bi is 1, i.e.,
    pi = ai + bi

## Slide 31: Carry-Lookahead Adder
Idea:
  Produce ci ahead of time instead of passing through (i-1) stages
Bit position
Carry
A
B
Sum
7 6 5 4 3 2 1 0
1 0 0 1 1 1 1
0 1 0 0 1 1 0 1 +
0 1 0 0 0 1 1 1
1 0 0 1 0 1 0 0
FA
FA
FA
FA
FA
Instead of RCA, use independent 1-bit FA-modules
no signal propagation through stages
Carry propagation in RCA

## Slide 32: Carry-Lookahead Adder
Instead of RCA, use n independent 1-bit FA-modules working in parallel;
no signal propagation through stages; directly generate all
carry-bits from inputs
C0
FA
A0
S0
B0
FA
A1
S1
B1
FA
A2
S2
B2
FA
A3
S3
B3
C4
C1
C2
C3
RCA
C0
FA
A0
S0
B0
FA
A1
S1
B1
FA
A2
S2
B2
FA
A3
S3
B3
C4
C1
C2
C3
CLA
Notes: In the example,
By looking at (A4,B4), we can say for sure that C5=0, no matter what C4 is.
By looking at (A2,B2), we can say for sure that C3=1.
C3, “generated” by (A2,B2) (or by A0,B0 if you wish), “propagated” as far as C4, and then got “killed” by (A4,B4)
The idea is, can we look at A(3..0) and B(3..0) and determine the value of C4 in one shot?

## Slide 33
Basic Signals
Generate signal: gi = aibi
Propagate signal: pi = ai + bi
ci+1 = gi + cipi
Carry recurrence

## Slide 34
Average Carry Propagation Length
Generate signal: gi = aibi
Propagate signal: pi = ai + bi
Given binary numbers with random bits, for each position i we have
Probability of carry generation = ¼ (both 1)
Probability of carry annihilation = ¼ (both 0)
Probability of carry propagation = ½ (different)
Average length of the longest carry chain for n-bit addition: O(log2n)

## Slide 35
Unrolling Carry Recurrence
ci = gi-1 + ci-1pi-1 =
= gi-1 + (gi-2 + ci-2pi-2)pi-1 = gi-1 + gi-2 pi-1 + ci-2pi-2pi-1 =
= gi-1 + gi-2 pi-1 + (gi-3 + ci-3pi-3)pi-2pi-1 =
= gi-1 + gi-2 pi-1 + gi-3 pi-2pi-1 + ci-3pi-3pi-2pi-1 =
= ….. =
= gi-1 + gi-2 pi-1 + gi-3 pi-2pi-1 + gi-4pi-3pi-2pi-1 + ….. +
+ g0p1p2…pi-2pi-1 + c0p0p1p2…pi-2pi-1 =
= gi-1 +  gk  pj + c0  pj
k=0
i-2
j=k+1
i-1
j=0
i-1

## Slide 36
4-bit Carry-Lookahead Adder
c4 = g3 + g2 p3 + g1 p2p3 + g0p1p2p3 + c0p0p1p2p3
c3 = g2 + g1 p2 + g0 p1p2 + c0p0p1p2
c2 = g1 + g0 p1 + c0p0p1
c1 = g0 + c0 p0
s0 = x0  y0  c0 = p0  c0
s1 = p1  c1
s2 = p2  c2
s3 = p3  c3
gi = aibi
pi = ai + bi
ci+1 = gi + cipi

## Slide 37: Carry Lookahead Adder
C1 = a0b0 + (a0+b0)c0 = g0 + p0c0
C2 = a1b1 + (a1+b1)c1 = g1 + p1c1 = g1 + p1g0 + p1p0c0
C3 = a2b2 + (a2+b2)c2 = g2 + p2c2 = g2 + p2g1 + p2p1g0 + p2p1p0c0
C4 = a3b3 + (a3+b3)c3 = g3 + p3c3 = g3 + p3g2 + p3p2g1 + p3p2p1g0 + p3p2p1p0c0
gi = aibi pi = ai + bi
a3 b3
g3
p3
a2 b2
g2
p2
a1 b1
g1
p1
a0 b0
g0
p0
c1
c2
c3
c4
c0
carry-bits
CLA logic
inputs
one AND-gate and
one OR-gate

## Slide 38: Carry Generation Logic

## Slide 39
4-bit CLA Logic
gi = aibi
pi = ai + bi
B: b3 b2 b1 b0
A: a3 a2 a1 a0
all carry-bits are generated directly from inputs;
one can thus use independent FA-modules, to produce the sum-bits in parallel!

## Slide 40
n-bit CLA Adder
Much faster than RCA
Critical path delay in an n-bit CLA?
Cost = O(?); delay O(?)

## Slide 41: Carry Lookahead Adder: Analysis
C1 = a0b0 + (a0+b0)c0 = g0 + p0c0
C2 = a1b1 + (a1+b1)c1 = g1 + p1c1 = g1 + p1g0 + p1p0c0
C3 = a2b2 + (a2+b2)c2 = g2 + p2c2 = g2 + p2g1 + p2p1g0 + p2p1p0c0
C4 = a3b3 + (a3+b3)c3 = g3 + p3c3 = g3 + p3g2 + p3p2g1 + p3p2p1g0 + p3p2p1p0c0
gi = aibi pi = ai + bi
a3 b3
g3
p3
a2 b2
g2
p2
a1 b1
g1
p1
a0 b0
g0
p0
c1
c2
c3
c4
c0
carry-bits
CLA logic
inputs
one AND-gate and
one OR-gate
Cost = O(?); delay = O(?)
cost = O(n3);
delay = O(1)
Independent FA blocks
sum outputs
2-level AND-OR logic

## Slide 42: Full Carry Lookahead
Theoretically, it is possible to derive each sum digit directly from the inputs that affect it
Full carry-lookahead adder is impractical for large n
s0
s1
s2
s3
b0
b1
b2
b3
a0
a1
a2
a3
cin
. . .

## Slide 43
Solution 1: n-bit Hybrid CLA Adder
Implementation of lookahead for the complete adder is impractical because of cost
    Divide n stages into smaller groups
    Full carry lookahead within each group
    Ripple carry among groups
    Compromise between cost and delay

## Slide 44: 12-Bit Hybrid Adder (CLA + RCA)
p,g
p,g
p,g
p,g
S0
S1
S2
S3
S4
S5
S6
S7
p,g
p,g
p,g
p,g
B0
B1
B2
B3
B5
B6
B7
B4
C0
C4
Carry Generator
Carry Generator
C8
S8
S9
S10
S11
p,g
p,g
p,g
p,g
B9
B10
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
B11
B8
Carry Generator
C12
0111
1101
0110
1001
1101
1010
0
B=
A=
Trade-off: cost versus delay
Another solution: 12-Bit Hybrid (RCA + CLA)??
Cost = O(?); delay = O(?)
CLA
RCA
Notes: The timing is not realistic. I have assumed:
  p_i and g_i computations take 1 cycle
  Carry generation block take 1 cycle to generate the last carry
  Hence, the second row shows T=2 (p,g calc + carry gen), while other rows show 1 cycle (only carry generation)

## Slide 45: CLA principle can be used recursively to build bigger adders => Carry-Lookahead Tree (CLT)
Example: A 16-bit adder - Use four 4-bit adders
It takes block g and p terms and cin to generate block-carry-bits
Use the CLA principle again to design lower level adders
CLA
CLA
CLA
CLA
CLA
Solution – 2
(CLA + CLA + …)
We have seen (i) CLA + RCA; (ii) RCA + CLA

## Slide 46
g15p15
16-bit 2-level Carry-Lookahead Tree (CLT)
CLA
c1
c2
c3
g[0,3]
p[0,3]
g0p0
g1p1
g2p2
g3p3
c0
CLA
c5
c6
c7
g[4,7]
p[4,7]
g4p4
g5p5
g6p6
g7p7
c4
CLA
c9
c10
c11
g[8,11]
p[8,11]
g8p8
g9p9
g10p10
g11p11
c8
CLA
c13
c14
c15
g[12,15]
P[12,15]
g12p12
g13p13
g14p14
c12
CLA
g[0,15]
p[0,15]
(Carry-lookahead tree - CLT)
Cost = O(?); delay O(?)

## Slide 47
64-bit 3-level Carry-Lookahead Tree (CLT)
g[16,19]
p[16,19]
c16
g[20,23]
p[20,23]
c20
g[24,27]
p[24,27]
c24
g[28,31]
p[28,31]
c28
CLA GEN
g[16,31]
p[16,31]
CLA GEN
CLA GEN
CLA GEN
CLA GEN
CLA GEN
c0
c31 c30 c29
c27 c26 c25
c23 c22 c21
c19 c18 c17
g[0,15]
p[0,15]
g[32,47]
p[32,47]
g[48,63]
p[48,63]
c32
c48
g[0,63]
p[0,63]

## Slide 48
Solution – 3: Carry-Select Adders (CSA)
Idea:
Compute sum-bits in parallel for two possible carry-bits;
When the previous carry actually arrives, just select the pre-computed “sum”
CLA: Looking ahead in time (pre-compute carry-bits)
CSA: Looking ahead in space (pre-compute sum-bits)

## Slide 49
k-bit Carry-Select Adder
sum-bits
carry-out
Units: cost and delay of a single 2-to-1 multiplexer

## Slide 50
Multi-level k-bit Carry-Select Adder
cost = ?
delay = ?
Other adder designs:
Carry-skip addition

## Slide 51
Pitfalls of CLA Adder
Implementation of lookahead for the complete adder is impractical because of cost
Analyze the implementation complexity of CLA

## Slide 52: CS 31007 Autumn 2021 COMPUTER ORGANIZATION AND ARCHITECTURE
Indian Institute of Technology Kharagpur
Computer Science and Engineering
Instructors
Rajat Subhra Chakraborty (RSC)
Bhargab B. Bhattacharya (BBB)
Lecture #19, #20: Computer Arithmetic
14 September 2021
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 53
Solution – 4: Tree-Based Adder
c4 = g3 + g2 p3 + g1 p2p3 + g0 p1p2p3 + c0 p0p1p2p3
c3 = g2 + g1 p2 + g0 p1p2 + c0 p0p1p2
c2 = g1 + g0 p1 + c0 p0p1
c1 = g0 + c0 p0
gi = aibi
pi = ai + bi
cn => last term would be p0p1p2……..pn-1
In general, the problem boils down to =>
How to compute efficiently in reasonable cost and time:
x0 , x0x1, x0 x1x2, x0x1x2 x3, …., x0x1x2x3 …xn-1
(Prefix-sum/product problem)
inputs
Recall: 4-bit CLA
In CLA, carry-logic cost grows @ O(n3) for n-input adders
ci+1 = gi + cipi

## Slide 54
4-bit Carry-Lookahead Adder
c4 = g3 + g2 p3 + g1 p2p3 + g0 p1p2p3 + c0 p0p1p2p3
c3 = g2 + g1 p2 + g0 p1p2 + c0 p0p1p2
c2 = g1 + g0 p1 + c0 p0p1
c1 = g0 + c0 p0
gi = aibi
pi = ai + bi
cn => last term would be p0p1p2……..pn-1
In general, the problem boils down to =>
How to compute efficiently in reasonable cost and time:
x0 , x0x1, x0 x1x2, x0x1x2 x3, …., x0x1 x2x3 …xn-1
(Prefix-sum/product problem)
inputs

## Slide 55: Why so fuss about prefix computation?
x
0
x
1
x
2
x
3
x0x1x2 x3 x0 x1x2 x0x1 x0
delay = O(n);
fanout: O(1);
cost = O(n)
x
4
x
5
x
6
x
7
*
*
*
*
*
2-input AND-gate
fanout
*
x0x1x2 ….x7
input
output
Use a serial chain …. … done!
However, its delay is again O(n), so the whole purpose of CLA design is defeated. Can we reduce delay, compromising cost and fanout?
Notes: - One disadvantage of this adder is the high fanout of the output of C7. Other adder structures like the Kogg-Stone tree are designed to reduce the fanout.

## Slide 56: Prefix tree: Basic idea
x
0
x
1
x
2
x
3
x0x1x2 x3 x0 x1x2 x0x1 x0
delay = O(log n);
fanout: O(n);
cost = O(nlog n)
*
*
*
*
x
4
x
5
x
6
x
7
*
*
*
*
*
*
*
*
2-input AND-gate
fanout
*
x0x1x2 ….x7
input
output
Large fanout slows down 0  1 or 1  0 transitions at logic nodes and thus may increase consumed power and signal delay indirectly
Notes: - One disadvantage of this adder is the high fanout of the output of C7. Other adder structures like the Kogg-Stone tree are designed to reduce the fanout.

## Slide 57: Prefix Tree: Logarithmic-Delay
x
0
x
1
x
2
x
3
x
4
x
5
x
6
x
7
x
8
x
9
x
10
x
11
x
12
x
13
x
14
x
15
s
0
s
1
s
2
s
3
s
4
s
5
s
6
s
7
s
8
s
9
s
10
s
11
s
12
s
13
s
14
s
15
1
2
3
4
5
6
Level
AND-gate
fanout
x0x1x2 x3 x0 x1x2 x0x1 x0
delay = O(log n);
fanout: O(log n);
adder cost = O(n2log n)?
*
Notes: - One disadvantage of this adder is the high fanout of the output of C7. Other adder structures like the Kogg-Stone tree are designed to reduce the fanout.

## Slide 58: Brent-Kung Parallel-Prefix Adder (log-delay)
ci+1 = gi + cipi
delay = O(log n);
cost = O(nlog n);
fanout: O(logn);
cost = O(n2log n)?
cost can further be improved

## Slide 59: Brent-Kung: Carry-Generation Tree for 8-Bit Adder
t
add
~
log
2
n
(g
0
,p
0
)
(g
1
,p
1
)
(g
2
,p
2
)
(g
3
,p
3
)
(g
4
,p
4
)
(g
5
,p
5
)
(g
6
,p
6
)
(g
7
,p
7
)
C
0
C
1
C
3
C
7
C
2
C
6
C
5
C
4
cost ~ O(nlog n)
delay ~ O(log n)
Notes: The tree generating C7 is called “forward tree”, and the rest is called “backward tree”
What do the inputs to module generating C5 mean?
[Par00] p. 101 shows a 16-bit Brent-Kung tree structure.

## Slide 60: Other Tree-Based Prefix Adders
Kogge-Stone Adder (16-Bit)
fanout: constant
delay = O(log n);
cost = O(nlog n);
- high wiring complexity
Notes: The tree generating C7 is called “forward tree”, and the rest is called “backward tree”
What do the inputs to module generating C5 mean?
[Par00] p. 101 shows a 16-bit Brent-Kung tree structure.

## Slide 61: Adder Design
Design considerations
Timing (delay)
Power/energy, heat dissipation
-- fan-in, fan-out, logic switching
Area (cost)
-- logic, wiring
logic depth
# fan-in
fan-out
# wire tracks
Timing
Power
Area
Notes: The tree generating C7 is called “forward tree”, and the rest is called “backward tree”
What do the inputs to module generating C5 mean?
[Par00] p. 101 shows a 16-bit Brent-Kung tree structure.

## Slide 62: Adding multiple numbers
can we do better?
Notes: The tree generating C7 is called “forward tree”, and the rest is called “backward tree”
What do the inputs to module generating C5 mean?
[Par00] p. 101 shows a 16-bit Brent-Kung tree structure.

## Slide 63: Carry-Save Addition: Adding multiple operands
Consider adding six numbers (4 bits each)
1001, 0110, 1111, 0111, 1010, 0110 (all unsigned +ve)
One way is to add them pair wise, getting three results, and then adding them again
1001 1111 1010 01111 100101
0110 0111 0110 10110 10000
01111 10110 10000 100101 110101
Other method is add them three at a time by saving carry
1001 0111 00000 010101 001101
0110 1010 11110 010100 101000
1111 0110 01011 001100 110101
00000 01011 010101 001101 SUM
11110 01100 010100 101000 CARRY
final sum

## Slide 64: CARRY-SAVE ADDER (addition of multiple operands)
Add four 4-bit integers, A, B, E, F
Cost = O(?); delay O(?)
can be made CLA

## Slide 65: Adding m, n-bit numbers with CSA and log-adder
Wallace tree;
Delay = O(logm + lg (n + logm))
Linear chain;
Delay = O(m + lg (n + m))
depth = log3/2m
LCA: Lookahead carry adder with log-delay (~CLT)
m
n
m
n

## Slide 66: Integer Multiplication
Multiplication Table

## Slide 67: Multiplication
  Multiplicand
  Multiplier
  Partial products
  Final sum
Base 10: 8 × 5 = 40
  => 32 + 0 + 8 = 40
How wide is the result?
  => log(n × m) = log n + log m
  => 32-bit × 32-bit = 64-bit result
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | × | 0 | 1 | 0 | 1
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | 0 | 0 | 0 | 0 | 
 |  | 1 | 0 | 0 | 0 |  | 
 | 0 | 0 | 0 | 0 |  |  | 
 | 0 | 1 | 0 | 1 | 0 | 0 | 0
+ 8
+ 5
- 8
+5
unsigned
2’s compl.
Can you notice the need for Carry-Save Addition? We need to add multiple numbers!

## Slide 68: CARRY-SAVE ADDER (addition of multiple operands)
Add four 4-bit integers, A, B, E, F

## Slide 69: CS 31007 Autumn 2021 COMPUTER ORGANIZATION AND ARCHITECTURE
Indian Institute of Technology Kharagpur
Computer Science and Engineering
Instructors
Rajat Subhra Chakraborty (RSC)
Bhargab B. Bhattacharya (BBB)
Lecture #21: Computer Arithmetic
16 September 2021
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 70: Unsigned Multiplication
Ai and Bi are all 0 or 1

## Slide 72: 4-Bit Array Multiplier Using Carry-Save Adders
Carry-Save Adder

## Slide 73: Array Multiplier Using Carry-Save Adders
CLT

## Slide 74: 16-bit Array Multiplier using Carry Sav-Adder
Conceptually straightforward
Fairly expensive hardware
[Courtesy: J. Hayes, Univ. of Michigan]

## Slide 75: Multiplication (Shift and Repeated Additions)
Mimic the multiplication process in hardware
1000
× 1001
1000
0000
0000
1000
1001000
Length of product is the sum of operand lengths
multiplicand
multiplier
product
§3.3 Multiplication

## Slide 76: Explanations
Multiplicand register is kept 64-bit wide because 32-bit multiplicand will be shifted 32 times to the left
  Requires a 64-bit ALU
Product register must be 64-bit wide to accommodate the result
Contents of multiplier register is shifted 32 times to the right so that each bit successively appears as the least significant bit (LSB) to be checked by the controller

## Slide 77: Multiplication Hardware
Initially 0
1000
× 1001
1000
0000
0000
1000
1001000
multiplicand
multiplier
product

## Slide 78: An Optimized Version of Multiplier
Perform steps in parallel: add/shift
One cycle per partial-product addition
Multiplier
(32-bits)

## Slide 79: Optimized Multiplication: Implementation

## Slide 80: Multiplication Example
0010 × 0110 = ? 0010 (+ 2, multiplicand); 0110 (+ 6, multiplier)
+12
logical shift

## Slide 81: Signed Multiplication
Recall
  For p = a × b, if either a < 0 or b < 0, then p < 0
  If (a < 0 and b < 0) or (a > 0 and b > 0) then p > 0
  Hence sign(p) = sign(a)  sign(b)
Hence
  Convert multiplier and multiplicand to positive number each
  Multiply two positive numbers
  Compute sign, convert product accordingly

## Slide 82: Multiplication: A Fundamental Question
Ai and Bi are all 0 or 1
What is the complexity of multiplying two n-bit integers?

## Slide 83: Integer Multiplication
Multiplication
Given two n-bit integers a and b, compute a  b
1
0
0
0
0
0
0
0
0
0
0
1
0
1
1
0
1
0
1
0
1
0
1
1
0
0
0
0
0
0
0
1
0
1
0
1
0
1
1
0
1
0
1
0
1
1
0
1
0
1
0
1
1
0
1
0
1
0
1
1
0
1
0
1
0
1
0
0
0
0
0
0
0
0
1
1
1
1
1
0
1
1
0
0
1
1
0
1
1
1
0
1
1
1
1
0

Ref: Jon Kleinberg and Éva Tardos, Algorithm Design
Slides by Kevin Wayn Copyright © 2005 Pearson-Addison Wesley
Q. Is school multiplication algorithm optimal?
School method
(n2) bit operations

## Slide 84: Integer Multiplication
Multiplication
Given two n-bit integers a and b, compute a  b
1
0
0
0
0
0
0
0
0
0
0
1
0
1
1
0
1
0
1
0
1
0
1
1
0
0
0
0
0
0
0
1
0
1
0
1
0
1
1
0
1
0
1
0
1
1
0
1
0
1
0
1
1
0
1
0
1
0
1
1
0
1
0
1
0
1
0
0
0
0
0
0
0
0
1
1
1
1
1
0
1
1
0
0
1
1
0
1
1
1
0
1
1
1
1
0

Q. Is grade-school multiplication algorithm optimal?
School method
(n2) bit operations
1952: Kolmogorov conjectured that any multiplication algorithm will take (n2) bit operations, i.e., it is asymptotically optimal
Andrey Nikolaevich Kolmogorov (1903 – 1987)
1960: Kolmogorov announced in a seminar at Moscow State University that it is indeed (n2)

## Slide 85: Integer Multiplication
Multiplication
Given two n-bit integers a and b, compute a  b
1
0
0
0
0
0
0
0
0
0
0
1
0
1
1
0
1
0
1
0
1
0
1
1
0
0
0
0
0
0
0
1
0
1
0
1
0
1
1
0
1
0
1
0
1
1
0
1
0
1
0
1
1
0
1
0
1
0
1
1
0
1
0
1
0
1
0
0
0
0
0
0
0
0
1
1
1
1
1
0
1
1
0
0
1
1
0
1
1
1
0
1
1
1
1
0

School method
(n2) bit operations
Anatoly Alexeyevich
Karatsuba (1937 – 2008)
1960: Within one week, Karatsuba disproved the claim, showing that multiplication can be done in O(n1.585) time!
Kolmogorov
1960: Kolmogorov announced in a seminar at Moscow State University that multiplication is indeed (n2)

## Slide 86: Karatsuba multiplication algorithm for two n-bit integers a, b
To multiply two n-bit integers a and b:
  Add two ½n bit integers.
  Multiply three ½n-bit integers, recursively
  Add, subtract, and shift to obtain result
1
2
1
3
3
Theorem: [Karatsuba-Ofman 1962] One can multiply two n-bit integers in O(n1.585) bit operations 
a
b
n/2
n/2
a0
a1
b0
b1
a1b0 + a0b1
=
(a1+ a0) (b1+ b0) ̶ a1b1 ̶ a0b0
Ref: Jon Kleinberg and Éva Tardos, Algorithm Design
Slides by Kevin Wayn Copyright © 2005 Pearson-Addison Wesley
Notes: Karatsuba: also works for multiplying two degree N univariate polynomials

## Slide 87: Multiplication of two n-bit integers a, b
Theorem: [Schönhage and Strassen] It is possible to multiply two n-bit integers in O(nlogn log logn) bit operations
Ref: D. E. Knuth, The Art of Computer Programming,
Vol. 2: Seminumerical Algorithms, Addison Wesley
Notes: Karatsuba: also works for multiplying two degree N univariate polynomials