## Slide 1: CS 31007 Autumn 2021 COMPUTER ORGANIZATION AND ARCHITECTURE
Indian Institute of Technology Kharagpur
Computer Science and Engineering
Instructors
Rajat Subhra Chakraborty (RSC)
Bhargab B. Bhattacharya (BBB)
Lecture #22: Computer Arithmetic
20 September 2021
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 2: Recap: Integer Multiplier using Repeated Add/Shift
Multiplier
(32-bits)
Can we expedite multiplication?
Handling negative numbers?
- Booth’s Algorithm

## Slide 3: Recall: Multiplication Example
0010 × 0110 = ? 0010 (+ 2, multiplicand); 0110 (+ 6, multiplier)
+12
logical shift

## Slide 4: Booth’s Encoding (valid for signed multiplication as well)
Recall old trick
  Example: 123454 × 9
   six partial products plus addition of six numbers
    123454 × 9 = 123454 × (10 – 1) = 1234540 – 123454
    Transform addition of six partial products to
    one shift and one subtraction!
Booth’s algorithm applies the same principle
  in binary we have just ‘1’ and ‘0’

## Slide 5: Booth’s Encoding
Multiply x by 0111
x (multiplicand); 0111 (multiplier) => x ×7
Search for a run of ‘1’ bits in the multiplier
  e.g. ‘0111’ has a run of 3 consecutive ‘1’ bits
  Multiplying by ‘0111’ (7 in decimal) is equivalent to multiplying by 8 and subtracting once, since
  x ×7 = x ×(8 – 1) = 8x – x =>(shift-left x, three times) - x
Hence, iterate right to left and look for “runs of 1”:
x × 111 = x × (1000 – 1) = (x ×23) – x
  Subtract multiplicand from product at first ‘1’
  Shift multiplicand by 3-bits on left and add to the partial product after the last ‘1’
  Do nothing for the consecutive 1-bits/in the middle, or for 0-runs (actually, we keep on shifting the product register)

## Slide 6: Booth’s Encoding for Multiplier
0 1 0 0 0 0 1 1 1 1 0 0
beginning of 1-run (10)
middle of 1-run (11)
end of 1-run (01)
0-run (00)

## Slide 7: Booth’s Algorithm
Current bit | Bit to right | Explanation | Example (multiplier) | Operation
1 | 0 | Begins run of ‘1’ | 00001111000 | Subtract/shift
1 | 1 | Middle of run of ‘1’ | 00001111000 | Nothing/shift
0 | 1 | End of a run of ‘1’ | 00001111000 | Add/shift
0 | 0 | Middle of a run of ‘0’ | 00001111000 | Nothing/shift

## Slide 8: Booth’s algorithm: Example
0010 × 1101 = ? 0010 (+ 2, multiplicand); 1101 (- 3, multiplier)
-6
op performed in the left half
arithmetic shift
initialization
start of
1-run
end of
1-run

## Slide 9: MIPS Multiplication
Two 32-bit registers for product
  HI: most-significant 32 bits
  LO: least-significant 32-bits
Instructions
  mult rs, rt / multu rs, rt
    64-bit product in HI/LO
  mfhi rd / mflo rd
    Move from HI/LO to rd
    Can test HI value to see if product overflows 32 bits
  mul rd, rs, rt
    Least-significant 32 bits of product –> rd

## Slide 10: So far covered in computer arithmetic…
Integer Number Systems and Overflow
Ripple-Carry Adder (RCA)
Carry-Lookahead Adder (CLA)
Hybrid Adder, CLT
Carry-Select Adder (CSA)
Brent-Kung’s Parallel Prefix Adder (PPA)
Carry-Save Adders (for adding multiple operands)
Integer Multiplication
Integer Division: Reading Assignment
Floating-Point Arithmetic and Hardware
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 11: Division
Implemented by successive subtractions
Result must verify the equality
Dividend = (Multiplier × Quotient) + Remainder
In biology, multiplication is accomplished by division!
Another powerful division method (Goldschmidt’s algorithm):
In computer science, division can be accomplished by multiplying a number with the reciprocal of the multiplier!

## Slide 12: Decimal division
What are the rules?
  Repeatedly try to subtract a multiple of divisor from dividend
  Record multiple (or zero)
  At each step, repeat with a lower power of ten
  Stop when remainder is smaller than divisor
 | 303
7 | 2126
 | -210
 | 26 -21 5

## Slide 13: Integer Division in Binary
Check for 0 divisor
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division
  Do the subtract, and if remainder goes < 0, add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
10
101
1010
-1000
10
n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor
§3.4 Division

## Slide 14: Division Hardware
Initially dividend
Initially divisor in left half

## Slide 15: Restoring Division

## Slide 16: Optimized Divider
One cycle per partial-remainder subtraction
Looks a lot like a multiplier!
  Same hardware can be used for both

## Slide 17: Faster Division
Can’t use parallel hardware as in multiplier
  Subtraction is conditional on sign of remainder
Faster dividers (e.g. SRT devision) generate multiple quotient bits per step
  Still require multiple steps

## Slide 18: MIPS Division
Use HI/LO registers for result
  HI: 32-bit remainder
  LO: 32-bit quotient
Instructions
  div rs, rt / divu rs, rt
  No overflow or divide-by-0 checking
    Software must perform checks if required
  Use mfhi, mflo to access result

## Slide 19: MIPS Architecture for Integer Arithmetic: Multiplication and Division

## Slide 20: CS 31007 Autumn 2021 COMPUTER ORGANIZATION AND ARCHITECTURE
Indian Institute of Technology Kharagpur
Computer Science and Engineering
Instructors
Rajat Subhra Chakraborty (RSC)
Bhargab B. Bhattacharya (BBB)
Lecture #23, #24: Floating-Point Arithmetic
21 September 2021
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 21: Floating Point: Format, Arithmetic, and Hardware Implementation
instruction set
software
hardware

## Slide 22
The IEEE Floating-Point Standard
So far as the theories of mathematics are about reality, they are not certain; so far as they are certain, they are not about reality. - Albert Einstein
A fundamental theoretical question: Can we prove Kepler’s Law of planetary motion by virtue of experiments?

## Slide 23: A computation error observed by a UG student led to the ACM Turing Award later ….
1953: Willian Kahan, a UG student of Math at the University of Toronto was simulating numerically the dynamics of the wing controller of an aircraft during take-off and landing
Observed certain unexpected results due to errors in computation
=> concept of floating-point (FP) arithmetic
=> principal architect behind IEEE 754 FP standard (1985)
=> Kahan honored with ACM Turing Award (1989)
William Kahan (1933 - )

## Slide 24: Floating-Point Representation
Used to represent real numbers: -34.98610-22, , e, 2
Defined by IEEE 754 Standard
--- Kahan (1985)
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)
  Infamous Intel Pentium Bug (1994) =>FDIV => loss of $300 Million

## Slide 25: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Normalized Significand is Mantissa with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1023
  Trade-off between range (E) and precision (M)
S
Exponent (E)
Mantissa (M)
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits
Fraction
Mantissa
 Significand

## Slide 26
IEEE 754 Single-Precision Floating-Point
Representation of floating point numbers in IEEE 754 standard:
single precision
1
8
23
sign
FP-exponent E:
excess 127 binary coding
mantissa:
sign + magnitude, normalized
binary significand w/ hidden
integer bit: 1.M
Actual exponent is e = E – 127
Floating-point exponent E = e + 127
S
E
M
FP-exponent (E) Actual exponent e
00000000 (0) Special use
00000001 (1) - 126
00000010 (2) - 125
…………. …….
01111111 (127) 0
…………. …….
11111110 (254) + 127
11111111 (255) Special use

## Slide 27: IEEE 754 floating-point standard
Leading “1” bit of significand is implicit
Exponent is “biased” to make comparison easier
  all 0s is smallest exponent; all 1s is largest
  bias of 127 for single precision and 1023 for double precision
  summary: (–1)sign ´ (1+significand) ´ 2exponent – bias
Example 1 (Encoding):
For a given decimal number, construct its FP-representation
  decimal: - 0.75
   binary: - 0.11 = - 1.1 x 2-1 (normalized)
   Floating-point exponent = - 1 +127 = 126 = 01111110
  IEEE single precision:
  - 0.75 = 1 01111110 10000000000000000000000

## Slide 28: Decoding a floating-point number
Sign indicated by first bit S  (-1)S
Subtract 127 from biased exponent E to obtain the actual exponent e = E - 127
Number in binary = (-1)S 1.M × 2e
S
E
M

## Slide 29: Example (Decoding)
Sign bit is zero: Number is positive
Biased exponent E = 1000 0000 |2 = 128;
Actual exponent e = E – 127 = 1  21
Significand  1.1 (restored the hidden bit)
The number = + 1.1  21 |2 = + 11 |2 = + 3.0|10
0
1000 0000
1000 0000 0000 0000 0000 000

## Slide 30: Example (Decoding)
Sign bit is one: Number is negative
Biased exponent E = 0111 1110 |2 = 126;
Actual exponent e = E – 127 = - 1  2-1
Significand  1.11 (restored the hidden bit)
The number = - 1.11  2-1 |2 = - 0.111 |2 = -0.875|10
1
0111 1110
11000000000000000000000000000

## Slide 31: Example (Encoding)
Represent –2 in FP-format
  Convert to binary: 10
  Normalize: 1.0×21
  Sign bit is 1
  FP-exponent is 127 + 1 = 128 = 10000000two
  Mantissa is 00…0
1
1000 0000
0000 0000 0000 0000 0000 000

## Slide 32
How do I represent zero then ?  1. M × 2E -127
FP-exponent (E) Actual exponent e
00000000 (0) Special use
00000001 (1) - 126
00000010 (2) - 125
…………. …….
01111111 (127) 0
…………. …….
11111110 (254) + 127
11111111 (255) Special use
* Any non-zero number that is smaller than the smallest normalized FP-number is a denormal number (consider magnitude only)
0/1
0000 0000
0000 0000 0000 0000 0000 000

## Slide 33: Single-Precision Range
Exponents 00000000 and 11111111 reserved
Smallest value
  Exponent: 00000001  actual exponent = 1 – 127 = –126
  Mantissa: 000…00  normalized significand = 1.0
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
  exponent: 11111110  actual exponent = 254 – 127 = +127
  Mantissa: 111…11  normalized significand ≈ 2.0
  ±2.0 × 2+127 ≈ ±3.4 × 10+38

## Slide 34: Double-Precision Range
Exponents 0000…00 and 1111…11 reserved
Smallest value
  Exponent: 00000000001  actual exponent = 1 – 1023 = –1022
  Mantissa : 000…00  norm. significand = 1.0
  ±1.0 × 2–1022 ≈ ±2.2 × 10–308
Largest value
  Exponent: 11111111110  actual exponent = 2046 – 1023 = +1023
  Mantissa: 111…11  norm significand ≈ 2.0
  ±2.0 × 2+1023 ≈ ±1.8 × 10+308

## Slide 35: Floating-Point Precision
Relative precision
  all mantissa-bits are significant
  Single: approx 2–23
    Equivalent to 23 × log102 ≈ 23 × 0.3 ≈ 6 decimal digits of precision
  Double: approx 2–52
    Equivalent to 52 × log102 ≈ 52 × 0.3 ≈ 16 decimal digits of precision

## Slide 36: Single-Precision Normalized Range
Exponents 00000000 and 11111111 reserved
Smallest value
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
  Largest value
  = ±(2.0 – 2-23) × 2+127 ≈ ±3.4 × 10+38
0/1
0000 0001
0000 0000 0000 0000 0000 000
0/1
1111 1110
1111 1111 1111 1111 1111 111
+1.0 × 2–126
-1.0 × 2–126
≈ +2.0 × 2+127
≈ -2.0 × 2+127
0
+ve-overflow
representable normalized +ve FP-numbers
-ve overflow
+ve
under-flow
-ve
under-flow
real line
representable normalized -ve FP-numbers

## Slide 37: Single-Precision FP-Denormal Numbers
Exponents 00000000 and 11111111 reserved
Smallest value (normalized)
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
  Denormal numbers (gradual underflow)
  = ± 0.M × 2-126 {min: ± 2-23 × 2-126; max: ± (1-2-23 ) × 2-126}
0/1
0000 0001
0000 0000 0000 0000 0000 000
0/1
0000 0000
M  0
+1.0 × 2–126
-1.0 × 2–126
≈ +2.0 × 2+127
≈ -2.0 × 2+127
0
overflow
representable normalized +ve FP-numbers
overflow
under-flow
under-flow
real line
representable normalized -ve FP-numbers

## Slide 38: Denormal FP-Numbers
Exponent = 000...0  hidden bit is 0
Smaller than normalized numbers
  allow for gradual underflow, with diminishing precision
Denormal with mantissa = 000...0
 +0, -0
N

## Slide 39: Infinities and NaNs
Exponent = 111...1, Mantissa= 000...0
  ± Infinity
  Can be used in subsequent calculations, avoiding need for overflow check
Exponent = 111...1, Mantissa ≠ 000...0
  Not-a-Number (NaN)
  Indicates illegal or undefined result
    e.g., 0.0 / 0.0, -3
  Can be used in subsequent calculations

## Slide 40: Floating Point Complexities
Operations are somewhat more complicated
In addition to overflow, we may have “underflow”
Accuracy can be a big problem
  IEEE 754 keeps three extra bits, guard, round, and sticky
  several rounding modes
  Non-zero number divide-by-zero yields “infinity”  overflow
  Non-zero number divide-by-infinity yields  underflow
  zero divide-by-zero yields “not a number (NaN)”
Implementing the standard can be tricky
Not using the standard can be even worse
Remember the 1994 Pentium FDIV bug; write-off cost US$ 300 M

## Slide 41: CS 31007 Autumn 2021 COMPUTER ORGANIZATION AND ARCHITECTURE
Indian Institute of Technology Kharagpur
Computer Science and Engineering
Instructors
Rajat Subhra Chakraborty (RSC)
Bhargab B. Bhattacharya (BBB)
Lecture #25: Tutorial on Floating-Point Arithmetic
23 September 2021
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 42: Floating-Point Addition
Consider a 3-digit mantissa binary example
  1.0002 × 2–1 + –1.1112 × 2–2
1. Align binary points
  Shift right the number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1 ; rightmost 1 is lost
2. Add significands (integer addition)
  1.0002 × 2–1 + –0.1112 × 2–1 = 0.0012 × 2–1
3. Normalize result & check for over/underflow
  1.0002 × 2–4, with no over/underflow
4. Round and renormalize if necessary
  1.0002 × 2–4 (no change) = 0.0625
overflow?
1.111
1.111
+ ------
11.110
How do you determine the sign of the result?

## Slide 43: Floating Point Addition
0
0111 1111
0000 0000 0000 0000 0000 000
0
1000 000
1000 0000 0000 0000 0000 000
0.1000 0000 0000 0000 0000 000
1.1000 0000 0000 0000 0000 000
A
B
A
B

## Slide 44: FP Adder Hardware
Step 1
Step 2
Step 4
Step 5
compare exponents
equalizing exponents
Integer addition
Step 3
normalize
round
Result

## Slide 45: Three Extra Bits for Internal Use
Three extra bits are added called Guard, Round, Sticky
  To achieve accurate arithmetic such as rounding of significand, otherwise some bits would have been lost during right shifts
  Reduces hardware without compromising precision
Guard, Round, Sticky
FP fields (32 or 64 bits)
Logical OR of all
shifted-out bits after R
S
E
M
1
1
G
R
S
1

## Slide 46: Guard Bit
When we shift bits to the right for alignment, some bits are lost
We may need to shift the result to the left for normalization after operation
Storing the lost bits shifted to the right will make results more accurate during normalization
Round and Sticky bits provide further handles for accurate rounding

## Slide 47: Guard, Round, and Sticky Bits
Two extra bits are needed for rounding
  Rounding performed after normalizing a result significand
  Round bit: appears after the guard bit
  Sticky bit: appears after the round bit (OR of all additional bits)
1.00000000000000000000000 × 25
-0.01111111111111111111111 1 1 00110 × 25(shifted right 7 bits)
0.10000000000000000000001 1 1 1 × 25 (sum)
1.00000000000000000000000 1 1 1 × 24 (normalized)
Round bit
Sticky bit
OR-reduce
Guard bit
Round bit
0.11111111111111111111110 × 24
1.11111111111111111111110 × 23

## Slide 48: Floating-Point Multiplication
Now consider a 3-digit mantissa binary example
  1.0002 × 2–1 × –1.1102 × 2–2 (0.5 × –0.4375)
1. Add exponents
  Unbiased: –1 + –2 = –3
  Biased: (–1 + 127) + (–2 + 127) = –3 + 254 – 127 = –3 + 127
2. Multiply significands
  1.0002 × 1.1102 = 1.1102  1.1102 × 2–3
3. Normalize result & check for over/underflow
  1.1102 × 2–3 (no change) with no over/underflow
4. Round and renormalize if necessary
  1.1102 × 2–3 (no change)
5. Determine sign: +ve × –ve  –ve
  –1.1102 × 2–3 = –0.21875

## Slide 49: Floating Point Multiplication

## Slide 50: Optimized Integer Multiplier
Perform steps in parallel: add/shift
One cycle per partial-product addition
  That’s ok, if frequency of multiplications is low

## Slide 51: FP Multiplier – Hardware Realization
integer multiplier

## Slide 52: FP Arithmetic Hardware
FP multiplier is of similar complexity to FP adder
  But uses a multiplier for significands instead of an adder
FP arithmetic hardware usually does
  Addition, subtraction, multiplication, division, reciprocal, square-root
  FP  integer conversion
Operations usually takes several cycles
  Can be pipelined

## Slide 53: FP Instructions in MIPS
FP hardware is Co-processor 1
  Adjunct processor that extends the ISA
Separate FP registers
  32 single-precision: $f0, $f1, … $f31
  Paired for double-precision: $f0/$f1, $f2/$f3, …
    Release 2 of MIPs ISA supports 32 × 64-bit FP reg’s
FP instructions operate only on FP registers
  Programs generally don’t do integer ops on FP data, or vice versa
  More registers with minimal code-size impact
FP load and store instructions
  lwc1, swc1,
    e.g., lwc1 $f8, 32($sp)

## Slide 54: FP Instructions in MIPS
Single-precision arithmetic
  add.s, sub.s, mul.s, div.s
    e.g., add.s $f0, $f1, $f6
Double-precision arithmetic
  add.d, sub.d, mul.d, div.d
    e.g., mul.d $f4, $f4, $f6
Single- and double-precision comparison
Branch on FP condition code true or false

## Slide 55: FP Example: °F to °C
C code:
float f2c (float fahr) { return ((5.0/9.0)*(fahr - 32.0)); }
  fahr in $f12, result in $f0, literals in global memory space
Compiled MIPS code:
f2c: lwc1 $f16, const5($gp) lwc2 $f18, const9($gp) div.s $f16, $f16, $f18 lwc1 $f18, const32($gp) sub.s $f18, $f12, $f18 mul.s $f0, $f16, $f18 jr $ra

## Slide 56: Summary
Computer arithmetic is constrained by limited precision
Bit patterns have no inherent meaning but standards do exist
  two’s complement
  IEEE 754 floating point
Computer instructions determine “meaning” of the bit patterns
Performance and accuracy are important so there are many complexities and implementation challenges in real machines

## Slide 57
Problem: Compute z = s/9 using only integer addition/subtraction, and shift; s: integer
Division operation not allowed
z = (s – z )/8
8z = s – z
z = s/9
z
Hardware requirement:
Only shifter and integer adder;
Iterate a few times to obtain a close approximation!